SECOND-ORDER PLASTIC-ZONE ANALYSIS OF STEEL FRAMES

Part II: Effects of Initial Geometric Imperfections and Residual Stress

Arthur R. Alvarenga and Ricardo A.M. Silveira

List of Figures:

Figure 1: The advanced analysis concept.

Figure 2: Member’s out-of-straightness modeling and influence.

Figure 3: Structure’s out-of-plumbness modeling and influence.

Figure 4: Residual stress set-up.

Figure 5: Residual stress diagrams of hot-rolled sections.

Figure 6: Residual stress diagrams of built-up sections.

Figure 7: Residual stress effect on Galambos and Ketter’s beam-column [25].

Figure 8: Residual stress modeling and influence.

Figure 9: Combination of initial geometric imperfections.

Figure 10: Advanced analysis of fixed-free column.

Figure 11: Steel portal frame.

Figure 12: Portal frame with members’ out-of-straightness.

Figure 13: Portal frame’s out-of-plumbness.

Figure 14: Combined initial geometrical imperfections of steel portal frame.

Figure 15: Collapsed configuration using advanced analysis.

Figure 16: Effect of opposite of the worst initial geometrical configuration model.

List of Tables:

Table 1: Collapse load factor of fixed-free column [23].

Table 2: Combination of initial geometric imperfections of steel portal frame.

Table 3: Advanced analysis of steel portal frame.

Figure 1: The advanced analysis concept.

(a) Out-of-straightness.          (b) Fixed-free column’ out-of-straightness.

(c) Equilibrium paths.

Figure 2: Member’s out-of-straightness modeling and influence.

(a) Out-of-plumbness.          (b) Fixed-free column’s out-of-plumbness.

(c) Equilibrium paths.

Figure 3: Structure’s out-of-plumbness modeling and influence.

(a) Cooled external parts.            (b) Still-hot parts cannot contract.              (c) Actual RS diagram.

Figure 4: Residual stress set-up.

Figure 5: Residual stress diagrams of hot-rolled sections.

(a) Rolled plates.      (b) Hot-cut plates.     (c) Welded rolled plates.  (d) Welded hot-cut plates.

Figure 6: Residual stress diagrams of built-up sections.

Figure 7: Residual stress effect on Galambos and Ketter’s beam-column [25].

(a) Residual stress on fiber.

(b) Equilibrium paths.

Figure 8: Residual stress modeling and influence.

(a) Out-of-straightness and out-of-plumbness.                (b) Reverse order (not recommended).

Figure 9: Combination of initial geometric imperfections.

(a) Out-of-straightness for left.             (b) Out-of-straightness for right.

(c) Equilibrium paths.

Figure 10: Advanced analysis of fixed-free column.

(a) Idealized frame.                      (b) Frame’s initial geometrical imperfections and data.

Figure 11: Steel portal frame.

(a) Left-left.                                             (b) Left-right.

(c) Right-left.                                          (d) Right-right.

Figure 12: Portal frame with members’ out-of-straightness.

(a) Left-left.                                       (b) Left-right.

(c) Right-left.                                    (d) Right-right.

Figure 13: Portal frame’s out-of-plumbness.

Figure 14: Combined initial geometrical imperfections of steel portal frame.

(a) Fixed-free column mounted as a frame.  (b) Portal frame study: worst initial geometrical model.

Figure 15: Collapsed configuration using advanced analysis.

(a) Opposite of the worst geometrical configuration.    (b) Correspondent collapsing deformed

geometry.

Figure 16: Effect of opposite of the worst initial geometrical configuration model.

.